## Slide 1: Conserving water and protecting water quality with rain barrels
Lisa Knerr, Environmental Program Manager
720-874-6525, Lknerr@arapahoegov.com

## Slide 2: Partners
Colorado State University
  One water Solutions Institute
    Colorado Stormwater Center (stormwatercenter.colostate.edu)
Splash (stormwater permittees for local awareness of stream health, splashco.org)
  Southeast metro stormwater authority
  Arapahoe county
Cherry Creek Stewardship Partners/Colorado Watershed Assembly

## Slide 3: Agenda
Why do we need to conserve water?
What is rainwater harvesting?
Colorado Rain Barrel Regulations
Types of Rain Barrels
Supplies Needed
How to install
Winterizing, Maintenance, FAQ
Decorating Your Barrel

## Slide 4: Why Conserve Water?
Notes: The Front Range is still growing
The average person using about 200 gallons of water per day on indoor and outdoor uses
Half of that is for outdoor use

## Slide 5: Residential Water Use
Average person in US uses 160-200 gallons per day
~Half of that Goes towards Outdoor Irrigation
Notes: Water rates are increasing
Some municipalities are restricting nonessential turf”—backyard turf is still okay
In 2022, the Colorado Legislature voted in a Cash for grass program. Grants will go to water providers. In 2023, $2M will not go that far, but it is a start…

## Slide 6: What can we do?
Fix leaks
Install/replace water efficient toilets, Clothes washers, showerheads, etc.
  Check for rebates from your water provider
  Look for WaterSense Products
Install/Replace Irrigation System Components
  Sprinkler Nozzles
  Irrigation Controller
Switch to Lower Water Landscaping
Rain Barrel(s)!!

## Slide 7: Rain Barrels also Reduce Stormwater pollution

## Slide 8: Residential Stormwater Pollution

## Slide 9: What can We Do?
Pick Up after your pet
Never put anything down the storm drain
Don’t Litter
Maintain your Vehicle
Go P free
Infiltrate more Stormwater Runoff with Rain Barrels!

## Slide 10: Reduced Stormwater Runoff= Reduced Stormwater Pollution

## Slide 11: What is Rain Water Harvesting
Collecting, storing, and putting rainwater runoff to use at your house.
Easy to collect via the existing gutter system

## Slide 12: Why Rainwater Harvesting?
It’s free!
Reduced demand for treated municipal water
Plants love it!
Chocolate Flower
Catmint

## Slide 13: Do we get enough rain?
Greenwood Village
  18 inches per year
  1 inch of rain x 1,000 sq ft roof=600 Gallons
  10,800 gallons per year

## Slide 14: What Can You do With Water from your Rain Barrel?
Vegetable Gardens
  Don’t directly water edible parts of veggies
Hanging plants
Greenhouse Plants
Landscaping

## Slide 15: Colorado Rain Barrel Regulations
In 2016, rainwater harvesting was legalized in Colorado for the first time
Maximum of 2 rain barrels with the combined storage of 110 gallons or less
Used for outdoor purposes like watering lawns, plants, or gardens
Container must have a sealable lid to prevent mosquito breeding
Never drink oR cook with water from a rain barrel
  It is untreated and may contain contaminates that could harm you or your pets if ingested

## Slide 16: Colorado Rain Barrel Regulation—Wells
Residences that have an exempt residential well permit do not have a limit on how much they can collect
Need a rooftop precipitation collection permit
Have to collect the water from the roof of your primary residence
Additional information with the division of water resources

## Slide 17: Considerations
Home Owner’s Associations
  Check with your HOA before you purchase your rain barrel
    May have some aesthetic or location requirements
  HOAs cannot prevent you from installing a rain barrel
Winterization needed
  Just like your sprinkler system
Think about spigot placement and overflow planning

## Slide 18: Types of Rain Barrels
Must have a lid
  Removable or an access point is best for cleaning
Should be made of Thick plastic
  No bags!
Should Have a spigot ~1-3” above the bottom of the barrel
  If lower, Can’t use the water
Should not have a top that holds water (mosquitoes!)
Should use a diverter
  Keeps Sediment, Leaves, etc. out of the bottom of the Barrel
  Easy winterization
Should have an overflow Mechanism
  If not using a Diverter

## Slide 19
Big holes in top
Spigot too high
Fixed lid (no way to clean barrel)
No overflow
Planter on top (holds water)
Spigot too high
No lid or access to clean barrel
No overflow
Could spring a leak!
No diverter or screen
No overflow

## Slide 20: Rain Barrel Materials
Plastic works best
  Be careful of metal drums!
Closed top
  Removable lid (only remove when cleaning!)
  Screw caps
UpcycleD barrels will need additional cleaning

## Slide 21: GEN 1(2004…..2016)

## Slide 22: Gen 2
Cheap plastic rain barrels ordered online (expensive!)
  Lasted 1-2 years
  Split on the bottom

## Slide 23: GEN 3 (2019)
So far, so good
  Backyard: Tricky downspout
  Added another spigot
    Now would use a dual spigot/Splitter
  Be careful of which side to Drill/Punch Out to add additional barrels

## Slide 24: GEN 4 (2021)
The best so far!

## Slide 25: Where to Buy
Colorado Rain Catcher
Container Reclaimer
Blue Barrel
Target, Sam’s, Walmart, Lowe’s, Home Depot, Amazon
BEWARE: Craigslist, Facebook Marketplace

## Slide 26: Supplies Needed
Food grade 55-Gallon Barrel with lid
  Container Reclaimer (Arvada): $30
  Colorado Rain Catchers (Ft. Collins): $50
Rain Barrel Connector Kit
  Colorado Rain Catcher ($39.50)
  Amazon ($36.92)
Total: ~$70-$90
  Colorado Rain Catcher Barrel and Connector Kit ($88)
Tools
  Level
  Drill
  Gloves
  Eye Protection
  Measuring Tape
  Pencil
  Etc.

## Slide 27: EarthmindeR Diverter
Pros
  Easy to install
  Do not need to remove the Downspout
  Cost effective
  Kit includes Hole saws and spigot
Cons
  Unable to see clogs
  Potential for clogging

## Slide 28: 1. Choose a Location
Walk around your home
  Find the downspout locations
Choose a location for your rain barrel
  Proximity to where you need the water
  Easy of making a level base in that area
  Catchment area: the amount of water you can collect from that downspout/roof area

## Slide 29: 1. Choose a location
Determine the square feet of the Roof area draining to the downspout
  Note how the Gutters slope
  Calculate
    Google the address
    Right click to “Measure Distance”
    Click to set the measurements and note the “Total Area” in ft2
Calculate the gallons that you can collect
  Catchment area (ft2) x Rainfall (ft) X 7.48 gal/ft3= Total Rainwater (gal)
  159 ft2 X 0.08 ft x 7.48 gal/ft3 = 95 gallons from a 1 inch storm for this small portion of the roof
    1 inch = 0.08 ft

## Slide 30: 2. Create a base
Rain barrels are very heavy! Children must always be supervised about rain barrels.
Select a flat location within 3 feet of a downspout
A Base Creates water pressure
Purchase a commercially available rain barrel stand or construct a simple base with wood, cinder blocks, bricks, or extra patio pavers
Full rain barrels weigh nearly 500 pounds!!

## Slide 31: 3. Drill a Spigot Hole in your Barrel
Sitting on the barrel gives you greater control
Measure 3 inches up from the bottom of the barrel and make a mark
Carefully drill the spigot hole using the Smallest hole saw
Insert the Fitting-use soap
Screw the spigot into the fitting by hand
Make sure the spigot is closed after you finish the installation

## Slide 32: 4. Drill a Fill Hole and Connect Hose
Consider the location of the barrel before drilling the fill hole
  The hole should be on the side of the barrel closest to the downspout
  Consider if you will add more barrels (will need room for the connector hose)
Measure 3 inches down from the top of the barrel and make a mark
Carefully drill the Fill hole using the medium hole saw
Insert the rubber fitting and hose

## Slide 33: 5. Install the Diverter in the Downspout
Warning: Always wear eye protection and gloves when drilling metal
Measure your downspout. Always drill on the 3 inch side of your downspout
  Your downspout could be 2”x3” or 3”x2”
Place your barrel on the stand with the spigot and fill hose in the correct location
Use a level to mark the height of the fill hose
The fill hose must be level to allow extra rain water to flow back out the downspout. If the fill hose is not level, water will overflow out of the top of the rain barrel (too high) or not fill (too low)
Carefully drill the Diverter hole using the Largest hole saw into the 3 inch side of the downspout

## Slide 34: 5. Install the Diverter in the Downspout
Install the flexifit diverter
  Squeeze the side of the rubber diverter and insert into the downspout
  The cup and arrow should be facing up
  Secure the diverter to the downspout with the two self-tapping screws
  Insert the fill tube to the diverter and into the barrel’s top hole
  Make sure the diverter is completely flush (no gaps!) and all the way inserted into the downspout
    Listen for the “pop”

## Slide 36: Test Your System

## Slide 37: Troubleshooting

## Slide 38: Troubleshooting
OR…

## Slide 40: 7. Optional: Install the tube for Two barrels
Kit sold separately
Installation Adjustment—drill an additional intake hole on first barrel
Connector pipe must be level and below the intake hole of the first barrel

## Slide 41: Winterizing Your Rain Barrel
Empty Barrel
Remove diverter and install winterization cap on downspout
  Tip: turn diverter upside down in downspout. Wiggle and squeeze the diverter.
  The winterization cap may be difficult to push into the downspout. Use self tapping screws to secure in place.
  Check the winterization cap for leaking.
Remove any debris from tubing.
Leave barrel in place or store for winter.
  Barrel may blow over if windy.

## Slide 42: Winterizing

## Slide 43: Winterizing

## Slide 44: Maintenance
Clean out gutters in spring before connecting barrel
  Gutter covers can help (optional)
Wait to connect the barrel until the second rain in the spring
Rinse out barrel to prevent algae blooms
  Can use a long handled brush
Use the water in your barrels

## Slide 45: FAQ
Will collecting water off of an asphalt roof leach pollutants?
Is it safe to use rainwater on a garden?
Will algae grow in my rain barrel?
How do I keep leaves and particles out of my barrel?
Can mosquitoes still get in my barrel?
  Mosquito dunk—harmless to pollinators and wildlife and safe on plants
Should I put weights on the top of my barrel?
  Probably not! Barrels can weigh up to 500 pounds and extra weight on the top might make it unstable.

## Slide 46: Decorating Your Barrel
Use sand paper (100 weight)
Wipe down and allow to dry
Spray plastic paint primer—paint will not stick with it!
  30 minute dry time
  Rust-oleum 2x ultracover primer for plastic
Create your own design
Can use cardboard stencils
For artistic barrels
  Use acrylic paint
  Protect your work by spraying with a paint sealer
Decorate BEFORE installation or remove rain barrel from house before decorating

## Slide 47: Decorating Your Barrel

## Slide 49: Accessorizing Your Barrel

## Slide 50: Questions?

## Slide 51: Pick Up Your Rain Barrels